INQUIRY SHEET  ____________________

for Multi-Turn Actuator Order placement

(MTN, MTP, MTNED, MTNPED)

| Fitting assembly | Quantity, pc.: |
| --- | --- |
| Type, DN, PN |  |  |
| Mechanical connection used with actuator |
| Pitch of pillars | A | ( 160 mm |  |
|  | B | ( 150 mm |  |
|  | C | ( 100 mm |  |
|  | D | ( 132 mm |  |
| Position „Closed“ | a | ( 30 mm |  |
|  | b | ( 74 mm |  |
|  | g | ( 130 mm |  |
| Thread in clutch | I | ( M20 x 1,5 |  |
|  | II | ( M16 x 1,6 |  |
|  | III | ( M10 x1 |  |
|  | ( Other |  |
| Actuator selection parameters |
| Axial force | Closing _____kN | Opening _____kN | Position-changing velocity __mm/min | Note |
| Surrounding conditions | Enclosure | Temperature, (C | Note |
|  | ( IP 55 ( IP 67 ( ______ | From | To | For actuators in non-explosive version, up to max. temperature +55°С |
|  |  | ( –25 ( –40 | ( –50 ( –60 ( ______ | ( +55 ( +70 ( ______ |  |
| Environments with explosion hazard | ( not required | ( ExdIIBT4 ( ExdIICT4 ( ExdeIIBT4 ( ExdeIICT4 ( __________________ | ExdIICT4 and ExdeIICT4 – only to temperature –25°С |
| Supply voltage | ( 3×380 (400) V, 50 Hz ( 1×220 (230) V, 50 Hz ( _______________ |
| Actuator functions | ( Open/Close | ( Regulation |
| Control signal | Discrete (voltage) signal ( ~250 V ( +24 V ( ________ |
|  | Analog signal ( Current 4-20 mA ( ___________________ |
|  | ( Digital signal - Profibus-DP protocol ( Digital signal - Modbus-RTU protocol |
| Feedback signal | ( Current transmitter 4-20 mA | ( Active | ( Passive |
|  | ( Resistance position transmitter (0-100Ω/0-10V) |
| Control system |
| Type of control system | ( Electromechanical | ( Electronic DMS2ED | ( Electronic DMS2 |
| Signalling unit | ( Included in assembly | ( Included in assembly | ( Included in assembly |
| Local control unit | ( Included in assembly | ( Included in assembly | ( Included in assembly |
| Built-in display | – | ( Included in assembly | ( Included in assembly |
| Position indicator | ( Mechanical (except actuators in explosion-proof design) | ( Built-in display function (included in assembly) | ( Built-in display function (included in assembly) |
| Reversing unit and electronic brake | ( Contactors ( Electronic brake | ( Contactors ( Contact-less ( Electronic brake | ( Contactors ( Contact-less ( Electronic brake |
|  | Note – electronic brake can be used in actuators with three-phase electric motor, with reversing unit and position controller. |
| Submitted by: |

# Text boxes

www.zpa-pecky.cz